## Slide 1: Optical Comb and Laser Locking
Mingda Li
July 2, 2023

## Slide 2
John L. Hall and Theodor W. Hänsch "for their contributions to the development of laser-based precision spectroscopy, including the optical frequency comb technique"

## Slide 3: Outline
Frequency comb
  Understand the comb
  Self-referencing method
What is laser locking?
  Wavemeter
  PDH locking
  Comb

## Slide 4: Part 1. Frequency comb

## Slide 5: What is frequency comb?
Mode-lock
ultrafast laser
Frequency comb
Fourier transformation
Arvanitaki, Searching for dilaton dark matter, 2015

## Slide 6: Understanding optical comb
What does the look like?
Thanks to Yanfei

## Slide 7: Understanding optical comb
What does the look like?
If we modulate the amplitude with a profile, then it will be…
Increasing , it will become pulse
Ultrafast pulse sequence

## Slide 8: Summary of the understanding
T. Fortier, E. Baumann, Communications Physics(2019)
Time domain
Freq domain

## Slide 9: What is frequency comb?
Mode-lock Ultrafast laser
Frequency comb
Fourier transformation
N. Picqué, T. W. Hänsch, Nature Photonics(2019)
However, the phase sometimes is not stable. How to lock it?
Phase is the difference between maximum of profile and maximum of E field.

## Slide 10: Self-referencing technique
T. Fortier, E. Baumann, Communications Physics(2019)
Self referencing technique is to make the different pulse to be phase locked. So, you beat note the f-2f to make the comb itself stable.
Difference frequency comb is a kind of comb to lock the to ZERO.

## Slide 11: Frequency comb for spectroscopy
I. Pupeza, C. Zhang, M. Högner, J. Ye, Nature Photonics(2021)
N. Picqué, T. W. Hänsch, Nature Photonics(2019)
Notes: Their fiber amplifier is 1020-1060, f_rep = 75MHz, 10^5 tunes
To enhancement the light to 7kW, increasing the power to get HHG, we use a cavity with FSR=75MHz, so the light can be accumulated in the cavity.

## Slide 12: How to mode-lock?
Q switch is only enough to provide ns. This is to tune the cavity Q.
Mode-locked laser is not Q-switch, it synchronize different signals rather than tuning the Q
  Using EOM: EOM can synchronize the phase of ν, ν − f and ν + f. If the modulator is driven at the same frequency as the cavity mode spacing Δν. Since the sidebands are driven in-phase, the central mode and the adjacent modes will be phase-locked together.
  Another way to think is, the modulation frequency f is corresponding to the period of phonon trip in cavity. Every time it can be increase to v+f, v+2f…
https://en.wikipedia.org/wiki/Mode_locking

## Slide 13: Using Comb to lock laser
To use the comb, you need to beat note it with the light you want to use.
Also you can pick up a tune by using grating. Or dicro. Or birefringent effect.

## Slide 14: Part 2. Laser locking

## Slide 15: What is laser locking?
E.g. Wavemeter, comb, cavity
E.g. DFB, dye laser, Ti: Sapphire…
Lock into zero-point
https://www.toptica.com/fileadmin/Editors_English/04_applications/10_application_notes/01_Application_Note_-_Phase_and_Frequency_Locking_of_Diode_Lasers/Phase_and_Frequency_Locking_of_Diode_Lasers.pdf
Measure difference,
PDH locking
Current, temperature, piezo
Two concerns
Accuracy
Stability

## Slide 16: Wavemeter
Wavemeter,
ECDL laser
Two concerns:
Accuracy: 2MHz
Stability: hmm yeah
Tune the wavelength by tuning current or temperature
https://www.toptica.com/fileadmin/Editors_English/04_applications/10_application_notes/01_Application_Note_-_Phase_and_Frequency_Locking_of_Diode_Lasers/Phase_and_Frequency_Locking_of_Diode_Lasers.pdf

## Slide 17: What kind of error signal do we like? (for cavity)
Two concerns:
Accuracy, need a steer slop
Stability, the other zero point
Accurate but not stable
Notes: 加一个线宽，然后信号浮动。PID很重要，能决定最后到达的线宽的极限，是一个因素。

## Slide 18: Pound-Drever-Hall (PDH) locking
Electro-optical modulator (EOM) can modulate the phase of light
the voltage to EOM
If we modulate the EOM with RF signal,

## Slide 19: Pound-Drever-Hall (PDH) locking
If we modulate the EOM with RF signal,
Do the Bessel function expansion:
sin: yellow, cos: blue
The power onto the photon detector:
Notes: https://zhuanlan.zhihu.com/p/451849194
A good reference.

## Slide 20: PDH locking of 798 & 846

## Slide 21: Thanks for attention!